## Slide 1: Rahman Ismail Sr. Software Architect
USB 3.0 Overview

## Slide 2: Agenda
What is USB 3.0
Connectors/cables
Physical Layer
Link Layer
Protocol Layer
Power Management
Summary

## Slide 3: USB 3.0 Features
10x performance increase over USB 2.0
Backward compatible
  Legacy devices continue to work when plugged into new host connector
  New devices work when plugged in legacy systems albeit at USB 2.0 speeds
  Existing class drivers continue to work
Same USB Device Model
  Pipe Model
  USB Framework
  Transfer types
Power Efficient
  Provides excellent power characteristics (especially for idle links)
    Both on the device and the platform
  Eliminate need for polling
Extensible
  Protocol designed to efficiently scale up
3
Notes: Devices operate exclusively in USB 3.0 SuperSpeed or USB 2.0, not both at the same time

## Slide 4: USB 3.0 Bus Architecture
Dual-bus architecture SuperSpeed bus operates concurrently with USB 2.0
  Electrically/mechanically backward & forward compatible
  Devices discovered/configured at fastest signaling rate
  Hubs provide additional connection points
SuperSpeed USB
  Dual simplex signaling
  Packets routed to device
  Hubs store and forward
  Asynchronous notifications
4

## Slide 5: SuperSpeed USB Layered Architecture
5
Notes: USB 3.0 SuperSpeed is layered. The following foils will take a bottoms up approach to talk about the layers. At a high level, they will talk about what goes into each layer, what happens to it in that layer and finally what comes out.

## Slide 6: USB 3.0 Connector & Cable Goals and objectives
Deliver low cost connectors and cable assemblies solutions to meet USB 3.0 architecture and performance needs
  Support 5 Gbps data rate
  Manage compatibility with USB 2.0
  Minimize connector form factor variations
  Contain EMI
  Comprehend ease-of-use aspects
6

## Slide 7: Connector interoperability summary
Receptacle | Plugs Accepted
USB 2.0 Standard-A | USB 2.0 Standard-A or USB 3.0 Standard-A
USB 3.0 Standard-A | USB 3.0 Standard-A or USB 2.0 Standard-A
USB 2.0 Standard-B | USB 2.0 Standard-B
USB 3.0 Standard-B | USB 3.0 Standard-B or USB 2.0 Standard-B
USB 3.0 Powered-B | USB 3.0 Powered-B, USB 3.0 Standard-B, or USB 2.0 Standard-B
USB 2.0 Micro-B | USB 2.0 Micro-B
USB 3.0 Micro-B | USB 3.0 Micro-B or USB 2.0 Micro-B
USB 2.0 Micro-AB | USB 2.0 Micro-B or USB 2.0 Micro-A
USB 3.0 Micro-AB | USB 3.0 Micro-B, USB 3.0 Micro-A, USB 2.0 Micro-B, or USB 2.0 Micro-A
7

## Slide 8: USB 3.0 Standard-A connector
Same interface as the USB 2.0 Standard-A connector, but with added pins for SuperSpeed USB signals
Complete compatibility with USB 2.0 Standard-A connector
Double-stacked connectors supported
VBUS
D+
GND
D-
GND
USB3_TX
USB3_RX
8

## Slide 9: USB 3.0 Standard-B connector
Defined for relatively large, stationary peripherals such as hard drives and printers
Visually different from USB 2.0 Standard-B connector
  But the receptacle accepts a USB 2.0 Standard-B plug
9

## Slide 10: USB 3.0 Micro connector family
Defined for hand held devices
Backward compatible with USB 2.0 Micro connectors
Based on USB 2.0 Micro-B connector with an extended portion for the SuperSpeed USB signals
USB 3.0 Micro-A and –AB connectors are identical to USB 3.0 Micro-B connector except for different keying
USB 2.0
Portion
USB 3.0
Portion
Micro-B
Micro-AB/A
10

## Slide 11: Cables
Unshielded twisted pair (UTP) cable used for USB 2.0 cannot be used for SuperSpeed USB
Shielded differential pair (SDP, twisted or twinax) is needed for SuperSpeed USB
  Signal integrity and EMI containment
11

## Slide 12: SuperSpeed USB Physical Layer
Symbols &
Sideband Signaling
12
Notes: The PHY layer is responsible for taking in bytes (data or control) and putting them onto the wire. In the process, the 8-bit data is converted to a 10-bit symbol which is scrambled. The data clock is spread and the clock is encoded with the data. The spreading and scrambling are used to minimize EMI. A requirement for an external cabled connection. The receiver recovers the clock from the data and reverses the scrambling and 8b/10b encoding process to pass back data and control bytes to the link layer. In addition, the PHY has the ability to turn off the physical layer driver and even the data clock. It uses side-band signaling to get the links out of these reduced power states. It is don this way to minimize power when not moving data. This same side-band signaling also is used for remote wakeup and to reset the link.

## Slide 13: Physical Layer
Support up to a 3 Meter cable
Based on existing specs
  Signaling similar to mix of high-speed serial buses (PCIe/SATA)
    2 differential pairs – dual simplex
  Retain sideband functionality (e.g. reset, wake) without additional wires
    Low Frequency Periodic Signaling (LFPS) – similar to PCIe beaconing
Retain USB Hot Plug functionality
  Rx termination for connect/disconnect detect
13
Notes: 13
PCIe-like signaling w/ eSATA like spread clock / CDR
Major differences
  SuperSpeed is not a common clock architecture
  SuperSpeed requires spread spectrum on both sides
  SuperSpeed requires Rx side equalization
  Jitter budgeting
    Clock jitter subsumed inside of Tx
    Channel jitter is more random
  No auxiliary pins for
    Connect/disconnect detection
    Link reset, PM state control, wake
Rx termination detection
Low Frequency Periodic Signaling (LFPS)

## Slide 14: SuperSpeed USB Link Layer
Packets &
Link Cmds
14
Notes: The link layer is responsible to take data from the protocol layer and package it up to send across the physical layer. It does this by making packets that are used for bus management, flow control and to move data. It also is responsible to endure that packet headers are moved reliably across the link. It appends header numbers and CRCs to ensure that the right header is received correctly. It is responsible to retry the header if not. It generates and interprets link commands to control the link PM state, frame packets etc. The USB 3.0 link is highly reliable – that is a packet with an undetected error is expected to get through only once every 400 years.

## Slide 15: Link Layer
Robust & Reliable
  Redundancy, advanced encoding techniques and retries
  >10-20 undetectable error rate for link commands
Effective Power Management
  Four link power states
  Either port can initiate link power state change
  Low Frequency Periodic Signaling (LFPS)
Link Commands
  Link flow control
  Link power state change
Packets
  Header Packets
    Store and forward
    Link level retries guarantee reliability
    Contain information consumed by link or host or device
  Data Packet
    Compound packet contains header plus data payload
15
Notes: 15
Redundancy is used on the construction of link commands and framing so that any one corrupted or missing symbol can be tolerated with no impact.

## Slide 16: SuperSpeed USB Protocol Layer
Headers &
Data
16
Notes: The protocol layer gets transactions from the application layer to move blocks of data. It is responsible to break those requests into bite size pieces and give the pieces to the link layer to send. It is responsible to check that the received packets are good (e.g. CRC) and retry them in not. It is responsible for processing notifications, sending system information (LTMs), sending timestamp packets etc. The protocol is asynchronous – that is, the host initiates a transfer and the device may either accept it and do it then or may say it is not ready. In the latter case, the device asynchronously notifies the host when it is ready. The SuperSpeed protocol has introduces the notion of streams. This extension of the bulk protocol allows a device to support multiple commands on a pipe and to service them out of order. This feature was driven to support the needs of Mass Storage, but was defined generically so it may be used by other device classes.

## Slide 17: Protocol Layer
Preserved legacy SW stack
  USB 2.0 transfer types (bulk, control, interrupt, isochronous)
Streams enhance bulk’s capabilities
  Multiple commands on a pipe
  Out of order completion
Optimized for good power management
  Routable Packet Architecture
  Asynchronous notifications
Efficient use of bandwidth
  Simultaneous IN / OUTs
17
Notes: 17
Backwards compatible with legacy SW stack
Routable – not broadcast
Asynch notifications - removes need to poll

## Slide 18: Packet Basics
Header & Data Packets
  Move between host and device
  Address triple: device address, endpoint number, direction
  Route String describes path between host and device
Host initiates ALL data transfers
Devices
  Either respond immediately or defer the packet
  Hubs proxy for target device by deferring packets routed to a downstream port whose link is not active
Deferred requests restarted asynchronously
  Device notifies host which responds with a new transfer request
Bus active only when moving data
18

## Slide 19: Example IN Transaction
19

## Slide 20: SuperSpeed USB Application Layer
Same as USB 2.0
20
Notes: The key here is that existing drivers will work. For example, there will be a demo today showing a Mass Storage device transferring data using the existing (unmodified) Windows Mass Storage driver. It should be noted that some device classes may be able to get better performance by using new capabilities of SuperSpeed such as simultaneous bi-directional transfers, streams etc.

## Slide 21: Power Management Overview

## Slide 22: Power Management Overview
Power Management is at all levels
  PHY layer, e.g. remote wakeup signaling
  Link layer, e.g. low power link state entry & exit
  Protocol layer, e.g. endpoint busy / ready notifications
  Devices, e.g. function suspend
  Hubs, e.g. “bubble up” link PM
  Hosts, e.g. ping / ping response messaging
Power efficiency at system level
  Async endpoint busy / ready notifications – no polling
  Packets routed, not broadcast
  Low power link states entered automatically when idle

## Slide 23: SuperSpeed USB Power Management Primitives
Physical Layer
  Lower power per bit
  Dual simplex - don’t need to turn around the bus
  Low Frequency Periodic Signaling
Link Layer
  Four Link States - trade lower power for increased latency
    U0: operational, U1: link idle with fast exit (PLL remains on)
    U2: link idle with slow exit (PLL may be off), U3: suspend
Protocol Layer
  Deferring & asynchronous device notifications
  Packets Pending flag
  Ping/Ping Response
  Selective Suspend
  Isochronous Timestamp packets
  Latency Tolerance Message
23
Notes:       LFPS – always on even when link in U3. Lowest power solution to detect wake, bring up a link etc.
      U0: operational, U1: link idle with fast exit (PLL remains on)
      U2: link idle with slow exit (PLL may be off), U3: suspend
      Controls data movement (ERDY/NRDY)
      LTMs aid system to chose deepest state consistent with device
      Ping/Ping-Response is used to wake a path for ISO transfers

## Slide 24: SuperSpeed USB Hubs
SuperSpeed USB hubs are more than port expanders
Hubs central to SuperSpeed USB power management
  A hub adjusts its upstream port link state based in its downstream ports’ link state
  A hub routes a downstream flowing packet only to the specified port
  A hub defers packets directed to ports whose links are not in the active state
  A hub has programmable inactivity timers on its downstream ports
  A hub only forwards multicast timestamp packets to downstream ports whose link is active
  A hub marks timestamp packets that are delayed
24
Notes:       Link states controlled by devices and/or HW inactivity timers
      Hubs propagate link state upstream - keeps fabric in lowest possible power state
      Intermediate hubs return deferred notifications to host – minimize stalls
      Isoch timing packets multicast only to links in U0
      Devices control data movement (ERDY/NRDY)

## Slide 25: Simple Deferring Example
25
Notes: Get rid of the words and turn into just a video with a voice over.

## Slide 26: Deferring Balances Performance with Power Management
26
Notes: Get rid of the words and turn into just a video with a voice over.

## Slide 27: Host Support for Bus Power Management - Interrupt Endpoints
Interrupt transfers must get completed within service interval
  Devices may use U1 / U2
  Host sends transfer far enough ahead of time to compensate for worst case link exit latency
Host stops interrupt endpoint activity upon receipt of an NRDY
  Resumes upon receipt of an ERDY
  No polling – links can enter U1 / U2 when there is no activity
Notes: Use here?
Refer to appropriate HC spec for how to tell host how far ahead of time to initiate transfer.

## Slide 28: Host Support for Bus Power Management Isochronous Endpoints and Timestamp TPs
Isochronous transfers must get completed within service interval
  Devices want to use U1 / U2 for improved power efficiency
  Devices must comprehend U1 / U2 exit latencies
Ping / ping response messaging
  Host sends a ping to isochronous device ahead of an isoch transfer
    Gets all links in path to device back to U0 prior to transfer
  Device responds with a ping response to host
    Host then schedules isochronous transfer
    Device keeps link in U0 until transfer occurs
  Host can perform other transfers while waiting for ping response
Timestamp packets sent at bus interval boundaries
  Only sent on downstream ports in U0
  U1 / U2 link inactivity timers ignore timestamp packets
Notes: Use Here?
Refer to appropriate HC spec for how to tell host how far ahead of time to send ping.

## Slide 29: Function Suspend and Device Suspend
Function suspend
  Individual functions* placed into function suspend independently
  Controlled by FUNCTION_SUSPEND feature selector
Device suspend
  Device-wide state coupled to U3
    Entered / exited intrinsically as a result of U3 entry / exit
      SetPortFeature(PORT_LINK_STATE U3)
  Device suspend entered regardless of function suspend state
Selective suspend also supported
  System software may initiate device suspend when all of a device’s functions are in function suspend
* Composite devices contain multiple functions
Notes: Use here?”

## Slide 30: SuperSpeed USB Power Management
Fine grain power management controlled by devices
  Devices control their own link state
    Host provides ‘packets pending transfer’ information to device
    When no transfers are pending, devices can put their link into a reduced power management state
  Hubs play key role
    Propagate link state upwards
    Forward packets only to the link in the direct path
    Forward Isochronous Timestamp packets only to active links and do not effect inactivity timers
Default power management policy
  Systems set by inactivity timers in downstream ports
30

## Slide 31: System Level Power Management Latency Tolerance Messaging
LTM enables system to enter deeper power saving states with cooperation of devices
Devices report the latency they can tolerate from the system in response to a request
  Send host LTM notification packet with latency value
Allows system to enter deeper sleep states when devices in system can tolerate it

## Slide 32: SuperSpeed USB Updates to the Specification
Same as USB 2.0
32

## Slide 33: Summary
Physical layer is based on existing industry specs
Maintained backwards compatibility
  Cabling/connector
    Standard A receptacles backward compatible with USB 2.0
    New B and Micro AB receptacles backward compatible with USB 2.0
  Devices – USB 2.0 support remains
  Software – Existing device drivers just work
  Hubs support both USB 2.0 & SuperSpeed USB devices
Link and Protocol optimized for Power Management
  U0-U3 link states
  Devices drive own link state, hubs propagate up
  Deferring and asynchronous notifications maximize opportunities for PM
  Hub inactivity timers provide coarser, but effective default PM
33

## Slide 34: Call to Action
Download & Review USB 3.0 Material
  Updated USB 3.0 Version 1.0 Specification
  Referenced documents
  Pipe Spec (www.developers.intel.com)
Device Link Power Management is a requirement
34
Notes: Pipe & xHCI
IF help promote, early access to integration lab, get tricks learned from our experiences
Early access to peripheral integration lab